# DELTA DVP Series PLC

# COMMUNICATION PROTOCOL for

# KELT-S

# This document describes the communications protocol that must be followed to communicate with the KELT-S Roof Controller. The information contained in this document is a summary of the information contained in the DELTA ELECTRONICS DVP communications document.

# Communication Interface: RS-232C- Communication between the Control PC and the PLC.

# Communication Protocol: The Serial port on the Control PC must have the following settings.		ASCII mode, Baud rate = 9600, Data length = 7bits, EVEN Parity, 1 Stop bit

- Communication Data Frame

| STX | Start character ‘:’ 3AHex |
| --- | --- |
| ADR 1 | Communication address: |
| ADR 0 | 8-bit address consists of 2 ASCII codes |
| CMD 1 | Command code: |
| CMD 0 | 8-bit command consists of 2 ASCII codes |
| DATA 0 | Contents of data: |
| DATA 1 | n(8-bit data consist of 2n ASCII codes. |
| ………. | n(37, maximum of 74 ASCII codes |
| DATA n-1 |  |
| LRC CHK 1 | LRC check sum: |
| LRC CHK 0 | 8-bit check sum consists of 2 ASCII codes |
| END 1 | End character: |
| END 0 | END 1 = CR (0D Hex) END 0 = LF (0A Hex0 |

- ADR Communication Address

Valid communication addresses are in the range of 0…31. Communication address equals to 0 means broadcast to all PLC, the PLC will reply normal message to the master device.

For example, communication to PLC with address 16 decimal:

(ADR 1, ADR 0)=’1’,’0’(’1’=31H, ‘0’ = 30H

For KELT-s ADR is 0 1

- LRC CHK Check Sum

LRC (Longitudinal Redundancy Check) is calculated by summing up, module 256, the values of the bytes from ADR1 to last data character then calculating the hexadecimal representation of the 2’s-complement negation of the sum.

It is important that the LRC is calculated correctly or the PLC will report a communications error.

For example, reading 1 word form address 0401H of the PLC with address 01H

| STX | ‘:’ |
| --- | --- |
| ADR 1 | ‘0’ |
| ADR 0 | ‘1’ |
| CMD 1 | ‘0’ |
| CMD 0 | ‘3’ |
| Starting data address | ‘0’ |
|  | ‘4’ |
|  | ‘0’ |
|  | ‘1’ |
| Number of data | ‘0’ |
|  | ‘0’ |
|  | ‘0’ |
|  | ‘1’ |
| LRC CHK 1 | ‘F’ |
| LRC CHK 0 | ‘6’ |
| END 1 | CR |
| END 0 | LF |

01H+03H+04H+01H+00+01H = 0AH

the 2’s-complement negation of 0AH is F6H

Exception response:

The PLC is been expected to return a normal response after receiving command messages from the master device. The following depicts the conditions that no normal response is replied to the master device.

The PLC does not receive the messages due to a communication error; thus the PLC has no response. The master device will eventually process a timeout condition.

The PLC receives the messages without a communication error, but cannot handle it, an exception response will return to the master device. In the exception response, the most significant bit of the original command code is set to 1, and an exception code explains the condition that caused the exception is returned.

An example of exception response of command code 01H and exception 02H:

Command message:

| Field Name | Example (Hex) |
| --- | --- |
| Heading | 3A |
| Slave Address | 01 |
| Function | 01 |
| Starting Address Hi | 04 |
| Starting Address Lo | 00 |
| Number of Points Hi | 00 |
| Number of Points Lo | 10 |
| Error Check ( LRC ) | EA |

Response message:

| Field Name | Example (Hex) |
| --- | --- |
| Heading | 3A |
| Slave Address | 01 |
| Function | 81 |
| Exception Code | 02 |
| Error Check ( LRC ) | 7C |

| Exception code: | Meaning: |
| --- | --- |
| 01 | Illegal command code: The command code received in the command message is not available for the PLC. |
| 02 | Illegal device address: The device address received in the command message is not available for the PLC. |
| 03 | Illegal device value: The device value received in the command message is not available for the PLC. |
| 07 | Check Sum Error Check if the check Sum is correct Illegal command messages The command message is too short. Command message length is out of range. |

- The format of data characters depends on the command. The available command codes are described as followed,

| Code | Name | Description |
| --- | --- | --- |
| 01 | Read Coil Status | S, Y, M, T, C |
| 02 | Read Input Status | S, X, Y, M,T, C |
| 03 | Read Holding Registers | T, C, D |
| 05 | Force Single Coil | S, Y, M, T, C |
| 06 | Preset Single Register | T, C, D |
| 15 | Force Multiple Coils | S, Y, M, T, C |
| 16 | Preset Multiple Register | T, C, D |
| 17 | Report Slave ID | None |

DELTA DVP-ES Series PLC DEVICE ADDRESS

| Device | Range | Effective Range | Address |
| --- | --- | --- | --- |
| S | 000~255 | 000~127 | 0000~00FF |
| S | 246~511 |  | 0100~01FF |
| S | 512~767 |  | 0200~02FF |
| S | 768~1023 |  | 0300~03FF |
| X | 000~377 (Octal) | 000~177 (Octal) | 0400~04FF |
| Y | 000~377 (Octal) | 000~177 (Octal) | 0500~05FF |
| T | 000~255 | 000~127 | 0600~06FF |
| M | 000~255 | 0000~1279 | 0800~08FF |
| M | 256~511 |  | 0900~09FF |
| M | 512~767 |  | 0A00~0AFF |
| M | 768~1023 |  | 0B00~0BFF |
| M | 1024~1279 |  | 0C00~0CFF |
| C | 000~255 | 000~127 232~255 | 0E00~0EFF |
| D | 000~255 | 000~599 1000~1143 | 1000~10FF |
| D | 256~511 |  | 1100~11FF |
| D | 512~767 |  | 1200~12FF |
| D | 768~1023 |  | 1300~13FF |
| D | 1024~1279 |  | 1400~14FF |

- Command Code 03:  Read Holding Registers

##### This command code is used to obtain the status from the KELT-S Roof Controller

The Roof Controller status is stored in memory locations D 110 – D 113.  The D in this case refers to the kind of memory and is not part of the address.  These memory locations are mapped to communications memory locations 106E to 1071 (Hex)

The following string must then be sent to the controller to request the status of the Roof Controller

| Field Name | (Hex) |
| --- | --- |
| Heading | : |
| Slave Address | 01 |
| Command code | 03 |
| Starting Address Hi | 10 |
| Starting Address Lo | 6E |
| Number of Points Hi | 00 |
| Number of Points Lo | 04 |
| Error Check ( LRC ) | 7A |
| END1 | CR |
| END0 | LF |

: 0103106E00047Acrlf  This string will not change and can be hard coded.

The PLC will return the following sting, :0101108xxxxxxxx00000000XXcrlf  The xs’ are the values of the requested addresses.  The XX is the LRC for the returned string

| Field Name | (Hex) |
| --- | --- |
| Heading | : |
| Slave Address | 01 |
| Command code | 03 |
| Bytes Count | 08 |
| Data Hi 106E | xx |
| Data Lo 106E | xx |
| Data Hi 106F | xx |
| Data Lo 106F | xx |
| Data Hi 1070 | 00 |
| Data Lo 1070 | 00 |
| Data Hi 1071 | 00 |
| Data Lo 1071 | 00 |
| Error Check LRC | XX |
| END1 | cr |
| END0 | lf |

The first four bytes in the Data part of the returned string will contain the ‘bit status’ of the roof controller and the next four bytes the timeout value that is in use for the communications delay function. The next 8 0s’ are from the reserved words that are not used at the moment.

Example

The Control PC requests the status of the roof controller by sending the string

:0103106E00047Acrlf

The PLC reply with the string

:010308003C01200000000097crlf

The :010308 section of the string is the header to indicate that controller 01 has executes a command number 03 and the data length is 8 bytes. 8 bytes are returned as 16 hexadecimal characters.

The next 4 characters 00 3C are the bit status and this can be broken up follow.

| Bit | Bit Value | HEX Value | Description |
| --- | --- | --- | --- |
| Bit 15 | 0 | 0 | Watchdog not tripped 1 = Watchdog tripped |
| Bit 14 | 0 |  | No closure due to Power Failure. 1 = Forced closure due to power Failure |
| Bit 13 | 0 |  |  |
| Bit 12 | 0 |  |  |
| Bit 11 | 0 | 0 |  |
| Bit 10 | 0 |  |  |
| Bit 9 | 0 |  | Lights not on. 1= Lights are on |
| Bit 8 | 0 |  |  |
| Bit 7 | 0 | 3 | Manual Close button not pressed 1= Button Pressed |
| Bit 6 | 0 |  | Manual Open Button not pressed 1= Button Pressed |
| Bit 5 | 1 |  | Forced Closure due to rain triggered 1= Forced closure |
| Bit 4 | 1 |  | It is raining 1= Raining 0 = Not raining |
| Bit 3 | 1 | C | The controller is set to Remote operation |
| Bit 2 | 1 |  | The roof is moving 1= Roof is moving |
| Bit 1 | 0 |  | The roof is not Open 1 = Roof is fully Open |
| Bit 0 | 0 |  | The roof is not Closed (the roof must be partly open since none of the limits are on) 1= Roof is fully closed |

The next four characters 0120 is the communications delay in seconds that is in use at the moment

The next four characters 0000 is the Power Failures delay in seconds that is in use at the moment.  In this case it has not been set.

The remaining 4 0s’ are the values in the reserved words that are not used.

The 97 is the LRC and the end is a CR and a LF.

Command Code 10:  Preset Multiple Registers

This command code is used to set the required commands for the KELT-S Roof Controller

Format of Command String

| Field Name | (Hex) |
| --- | --- |
| Heading | : |
| Slave Address | 01 |
| Command code | 10 |
| Starting Address Hi | 10 |
| Starting Address Lo | 64 |
| Number of Register Hi | 00 |
| Number of Register Lo | 04 |
| Byte Count | 08 |
| Data Hi | XX |
| Data Lo | XX |
| Data Hi | XX |
| Data Lo | XX |
| Data Hi | XX |
| Data Lo | XX |
| Data Hi | XX |
| Data Lo | XX |
| Error Check (LRC | Calculate |
| END1 | CR |
| END0 | LF |

Example: Required actions.  Close the Roof, rain detector on and switch the lights on

The firsts word will be encoded to

| Bit | Bit Value | HEX Value | Description |
| --- | --- | --- | --- |
| Bit 15 | 1 | 8 | Reset Watchdog Always send 1. If the roof was closed due to a timeout setting this bit will reset it. |
| Bit 14 | 0 |  | 0= Do not to load new Power failure delay 1= load Power failure delay |
| Bit 13 | 0 |  | 0 = Do not load new watchdog delay 1= load watchdog delay |
| Bit 12 | 0 |  |  |
| Bit 11 | 0 | 2 |  |
| Bit 10 | 0 |  |  |
| Bit 9 | 1 |  | 1 = Switch the lights on 0 = switch lights off |
| Bit 8 | 0 |  |  |
| Bit 7 | 0 | 1 | 0 = Normal 1= Reset Forced Power Failure closure |
| Bit 6 | 0 |  | No need to select remote operations. The mode can be determined by reading the status and is only done once. 1= Select remote control 0 = use current setting |
| Bit 5 | 0 |  | 0 = Normal 1 = Reset Forced Rain Closure |
| Bit 4 | 1 |  | Rain sensor is on. Must be a 1 for every transmission of a command string if the sensor is to stay on. 1 = enable forced rain closure 0 = disable forced rain closure |
| Bit 3 | 0 | 1 |  |
| Bit 2 | 0 |  |  |
| Bit 1 | 0 |  | Open Roof command 1 = Open Roof |
| Bit 0 | 1 |  | Close the roof command 1 = Close roof |

The above is 8211 Hex.  The communications delay is assumed to be 0125 seconds.  This number will however not be used since bit 13 is a 0. The power Failure delay is set to 0000 seconds.  This number will however not be loaded since bit 14 is a 0.

PC→PLC  “ : 01 10 10 64 00 04 08 82 11 01 25 00 00 00 00 B6 CR LF”

Header				DATA				LRC + END

The spaces in the above string are only for clarity and not part of the data string.

| Field Name | (Hex) |
| --- | --- |
| Heading | : |
| Slave Address | 01 |
| Command code | 10 |
| Starting Address Hi | 10 |
| Starting Address Lo | 64 |
| Number of Register Hi | 00 |
| Number of Register Lo | 04 |
| Byte Count | 08 |
| Data Hi | 82 |
| Data Lo | 11 |
| Data Hi | 01 |
| Data Lo | 25 |
| Data Hi | 00 |
| Data Lo | 00 |
| Data Hi | 00 |
| Data Lo | 00 |
| Error Check (LRC | B6 |
| END1 | CR |
| END0 | LF |

If the above command is accepted by the PLC, the following reply will be returned.

PLC→PC  “: 01 10 10 64 00 04 77 CR LF”

| Field Name | (Hex) |
| --- | --- |
| Heading | : |
| Slave Address | 01 |
| Command code | 10 |
| Starting Address Hi | 10 |
| Starting Address Lo | 64 |
| Number of Registers Hi | 00 |
| Number of Registers Lo | 04 |
| Error Check ( LRC ) | 77 |
| END1 | CR |
| END0 | LF |

After the command is issued the control PC may issue a status request to determine the status of the controller and if the command is executed.

It is not necessary that a command must be followed by a status request.  The commands and status request can be issued in any order and there is no time constrain on when it can be done.  The only constraint is that a ‘send command’ must be issued at least once within the time set for the watchdog or the roof will close.  If there is no change in the command the user can simply send the last command again.  It is important that bit 15 of every command is set to reset the watchdog timer.